## Slide 1: Pacemaker Demo on Leon3
UCInspire Program
Han Wang

## Slide 2
My work:
  Understood the basic concept and working principle of the pacemaker by reading the VHDL, C code, and some reference.
  Translated the hardware pcores to software code.
  Set the communication between the board and PC by using TCP/IP module and Socket programming.
  Developed a MATLAB GUI.

## Slide 3
My work:
  Understood the basic concept and working principle of the pacemaker by reading the VHDL, C code, and some reference.
  Translated the hardware pcores to software code.
  Set the communication between the board and PC by using TCP/IP module and Socket programming.
  Developed a MATLAB GUI for doctoral configuration.

## Slide 4: Introduction
Pacemaker is a small device with two parts — a generator and wires (leads, or electrodes) — that's placed under the skin in your chest to help control your heartbeat.
Normal heart beat: 60-100 /min
Pacemakers would maintain your normal
heart beat.
Notes: Normal heart beat is of paramount importance
先介绍心脏：The beating of the heart can be divided into two processes
电信号：electric signal trigger one heart beat

## Slide 5: Basic concept of pacemaker programming
Atrial-Ventricular Interval (AVI):
The AVI is the time interval between an atrial paced or sensed event, and the delivery of a ventricular pacing stimulus.
Notes: 电信号：electric signal trigger one heart beat

## Slide 6: Basic concept of pacemaker programming
Atrial Escape Interval (AEI) or Ventricular-atrial interval (VAI):
The AEI is the time period from a ventricular event (intrinsic or paced) to an atrial pace.
Notes: 电信号：electric signal trigger one heart beat

## Slide 7: Basic concept of pacemaker programming
Ventricular Refractory Period (VRP):
VRP is the time interval following a ventricular event (sensed or paced) during which signals in the ventricle are not sensed.
Notes: 电信号：electric signal trigger one heart beat

## Slide 8: Basic concept of pacemaker programming
Post Ventricular Atrial Refractory Period (PVARP):
PVARP is the time interval following a ventricular event (sensed or paced) during which signals in the atrium are not sensed
Notes: 电信号：electric signal trigger one heart beat

## Slide 9: Basic concept of pacemaker programming
Total Atrial Refractory Period (TARP):
AVI and PVARP together form the Total Atrial Refractory Period.
Notes: 电信号：electric signal trigger one heart beat

## Slide 10: Working Principle
VAI
VAI
VAI
Atrium
Ventricle
Notes: Timer overflow

## Slide 11
Notes: Structure of the pacemaker
Works sync

## Slide 12: Original C code

## Slide 13: Original C code

## Slide 14: Original C code

## Slide 15: Original C code

## Slide 16: Original C code

## Slide 17: Functions
Monitor the patience’s heart beat
Sense the atrial and ventricular beat
Generate the atrial or ventricular beat
Record the heart beat history data
Communication
Be configurable
And more…

## Slide 18
My work:
  Understood the basic concept and working principle of the pacemaker by reading the VHDL, C code, and some reference.
  Translated the hardware pcores to software code.
  Set the communication between the board and PC by using TCP/IP module and Socket programming.
  Developed a MATLAB GUI for doctoral configuration.

## Slide 19: POSIX Thread
Runs in parallel
Has very good portability
Function()
Do some work
Function
pthread_creat()
Do some work
Muti-thread
VS
Can not run in parallel

## Slide 20
How could threads get synchronization?
  Mutexes
  Conditional variable
Thread A
Thread B
Lock
Signal
unlock
Lock
Wait
unlock
Conditional
variable
Notes: Crucial area

## Slide 23
LEON3 Processor
+
RTEMS
RTEMS: real-time operation system
Designed for real-time, embedded systems and to support various open API standards including POSIX
Architectures: ARM, Freescale Cold Fire, DSPs, LEON
Platform

## Slide 24
My work:
  Understood the basic concept and working principle of the pacemaker by reading the VHDL, C code, and some reference.
  Translated the hardware pcores to software code.
  Set the communication between the board and PC by using TCP/IP module and Socket programming.
  Developed a MATLAB GUI for doctoral configuration.

## Slide 25: Communication method selection
Programming
UART
Build-in JTAG
Data transmission
UART
Ethernet

## Slide 26: Communication method selection
Programming
UART
Build-in JTAG
Data transmission
UART
Ethernet

## Slide 27
Ethernet
  Fast
TCP/IP
Reliable
Socket Programming
Easy to use

## Slide 29
Some Problems:
  1) The number of bits transferred must be determined, but VAI, AVI and heart rate could have different number of digits
  e.g. AVI could be 120ms or 90ms
  Solution:
  120 ‘120’, 90 ’990’
  2) It is not a Full Duplex communication. How to receive command from the client during the transfer process and how to determine the right order of the data?
  Solution:
  Use a token to make it in good order.

## Slide 30
Receiving
Sending
Token Ring
Token=2
Send AVI
Token=0
Receive the command
Token=1
Send VAI
Token=3
Send heart rate
Atrial thread
AVI thread
VAI thread
Comn thread

## Slide 31
My work:
  Understood the basic concept and working principle of the pacemaker by reading the VHDL, C code, and some reference.
  Translated the hardware pcores to software code.
  Set the communication between the board and PC by using TCP/IP module and Socket programming.
  Developed a MATLAB GUI for doctoral configuration.

## Slide 32
Matlab GUI

## Slide 34
My gains:
  Experienced doing research in the United States
  Gradually adapted to independent life in a unfamiliar environment
  Met many outstanding people and known different field of study
  Strengthened the determination of studying in the United States

## Slide 35
Special Thanks to
Prof. Fadi Kurdahi
And
Dr. Minjun Seo